## Slide 1: Hardware Triggered Scanning: Introduction
Philip Taylor, Emma Arandjelovic
Observatory Sciences Limited

## Slide 2: Course Aims
Get to know the functionality provided by the hardware triggered scanning stack
Understand the architecture, and acquire basic knowledge of all the components
Get hands-on experience of setting up scans
Learn how to debug common problems!

## Slide 3: Course Content
Introduction and demo
Overview of the hardware
Low level control and data acq. concepts
Scan configuration
Experiment control and data processing
Practical exercises

## Slide 4: Grid Scanning Overview
Move sample in X and Y to scan it through the beam
Rewind at the end of each row or reverse direction (‘alternate/snake’ scan)
Data acquisition can be done using:
Software step scan
Hardware step scan
Continuous scan
Continuous scans are much faster! But also complex…

## Slide 5: Framework Motivation
Growing need for fast, continuous scanning
Complex trajectories – not just grids!
Need for on-the-fly visualization of data
Desire for a generic solution

## Slide 6: Hardware Components
T
Motion trajectory
control
Motor drive
Encoder signal

## Slide 7: Hardware Components
T
Motion trajectory
control
Data capture
Detector
images
Motor drive
Encoder signal

## Slide 8: Hardware Components
T
Motion trajectory
control
Flexible triggering, and fast position capture
Data capture
PandABox
Transformed trigger pulses
Detector
images
Motor drive
Encoder signal
Raw trigger signals

## Slide 9: Hardware Components
T
Motion trajectory
control
Flexible triggering, and fast position capture
Data capture
PandABox
Transformed trigger pulses
Averaged position data
Detector
images
Motor drive
Encoder signal
Raw trigger signals

## Slide 10: Software Components
Data Analysis WorkbeNch
- Analysis and visualization
Generic Data Acquisition
- Experiment setup and supervision
Malcolm
- Scan configuration
Experimental Physics & Industrial Control System
- Low level control of hardware

## Slide 11: System Architecture Control Flow
GDA
Malcolm
EPICS
PandA
Delta Tau
Detector
GUI / scripts
Channel access
pvAccess
AreaDetector
driver
PMAC
driver
TCP socket
Custom setup only

## Slide 12: System Architecture Data Flow
GDA
EPICS
PandA
Detector
Data Processing
HDF
NeXus File
Position
data
Frames
HDF
Metadata

## Slide 13: Test Rig

## Slide 14: Test Rig
Beamline in a box!
  Light illuminated ‘sample’
  Two stepper motors (θ and X)
  DT Turbo Clipper controller
  Allied Vision Mako camera
  PandA electronics
  PC with full software stack for testing and training

## Slide 15: Test Rig

## Slide 16: Demo Application
Grid scan in θ and X
‘Snake’ style
1 | 2 | 3 | 4
8 | 7 | 6 | 5
9 | 10 | 11 | 12
16 | 15 | 14 | 13
x-axis: rotation (θ)
y-axis: linear translation (X)

## Slide 17: Camera View
Camera configured to capture a thin slice – each image is 1936 x 20 array
Images used to reconstruct the sample

## Slide 18: Stage 1: Setup scan
Open GDA mapping perspective
rotation axis
translation axis
exposure time
Open DET panel from the Test Rig panel and select MJPG tab

## Slide 19: Stage 2: Start scan
Hit ‘Queue scan’
Motors move to initial positions
Scan starts
Images are acquired
Watch the data acq. in GDA

## Slide 20: Stage 3: Check the data

## Slide 21
To improve the image:
Higher resolution (AKA more images)
  Increase stagea points  180
  Increase stagex points  40
Process the image
If you see “jaggy edges” on the sinogram, try turning off alternating

## Slide 22: Stage 4: Check the data
Screenshot of improved data

## Slide 23: Stage 5: Add processing
/dls_sw/htss/software/gda_var/processingTemplates/mean_integrate.nxs

## Slide 24: Stage 6: Check the data

## Slide 25: Stage 7: visualhulls
App Name must be exactly “visualhulls”
Config File: $HOME/vh.json

## Slide 26: Stage 7: visualhulls
Right click on the visualhulls .nxs in Mapped Data
Transfer > DataVis
Check the visualhulls.nxs file just created in Data Files
Select /processed/result and Plot Type “Volume” in Datasets

## Slide 27: Stage 8: Check the data

## Slide 28: Stage 9: Improve visualhulls
start
stop
height/2 = cor