## Slide 1: Hardware Triggered Scanning: EPICS Layer
Philip Taylor, Emma Arandjelovic
Observatory Sciences Limited

## Slide 2: Software Stack: Reminder
Data Analysis WorkbeNch
- Analysis and visualization
Generic Data Acquisition
- Experiment setup and supervision
Malcolm
- Scan configuration
Experimental Physics & Industrial Control System
- Low level control of hardware

## Slide 3: EPICS Responsibilities
Motion control interface
Detector setup
File saving
On training rigs, a single IOC BLxx-EA-IOC-01 takes care of everything
Beamlines may use multiple IOCs

## Slide 4: Motion Control
EPICS pmac module takes care of:
  Co-ordinate system configuration
  Sending trajectory profiles to the controller
Motion parameters defined in a motor record for each axis:
  MRES: motor resolution
  VMAX: maximum velocity
  ACCL: acceleration time

## Slide 5: Coordinate system

## Slide 6: AreaDetector
EPICS framework for controlling detectors
  Provides a standard, general-purpose interface
  Supports a wide variety of detectors
  Real time data analysis and processing
  Configurable plugin architecture
  Data passed through plugin chain in an NDArray
    N-dimensions (up to 10) with attached metadata (NDAttributes) associated with the frame
  http://cars9.uchicago.edu/software/epics/areaDetector.html

## Slide 7: AD Architecture
Source: Mark Rivers, Using AreaDetector

## Slide 8: AD Plugins
    Plugins receive a copy of each NDArray via a callback
    They can in turn be sources of NDArray callbacks
    Plugins can also attach NDAttributes to the data
    Chain can be ‘rewired’ on the fly and plugins enabled/disabled

## Slide 9: Plugin Chain Example
Detector Driver
HDF5 Plugin
MJPG Plugin
Statistics Plugin
ROI Plugin
Processing Plugin
HDF5 Plugin
Small region of interest streamed for live viewing
Total intensity attached for saving as a dataset
Background removed

## Slide 10: Detector Setup
Each detector has an AreaDetector driver
At scan start, this sets up parameters such as:
  Exposure time

## Slide 11: Detector Setup
Each detector has an AreaDetector driver
At scan start, this sets up parameters such as:
  Number of images

## Slide 12: Detector Setup
Each detector has an AreaDetector driver
At scan start, this sets up parameters such as:
  Trigger mode

## Slide 13: Detector Setup
Each detector has an AreaDetector driver
At scan start, this sets up parameters such as:
  Frame size

## Slide 14: Data Files
Data is saved in the hierarchical HDF format
Metadata is stored in the form of user-defined, named attributes attached to groups and datasets
NDAttributes
/entry
detector
sum
Designed for:
  Flexible, efficient I/O
  high volume and complex data
Groups -
Datasets -

## Slide 15: SWMR Mode
Single Writer Multiple Reader
Process data as it’s written to file
Requires POSIX compliant file system (N.B. NFS is NOT POSIX compliant)
HDF5 File
Writer
Reader
…that can be read by a reader…
New data elements…
… are added to a dataset in the file…

## Slide 16: HDF5 Considerations
Flush rate determines how often data is flushed to disk (controlled by Malcolm)
HDF Datasets are chunked: divided into equally sized blocks
  Each chunk stored contiguously in the file
  Avoids need to read in the whole file
  Allows datasets to be extendible
  Enables compression
  Chunk size is configured in the HDF5 plugin
See HDF5 Advanced Topics Tutorial

## Slide 17: Read/Write Performance
Performance GREATLY (up to 1000 times!!) affected by:
  Chunking settings
  Compression
  Flush rate
Settings must be optimised for the experiment
Consider BOTH read and write performance
This is a complex issue!
Never set a chunk size of 1!

## Slide 18: File Saving
NDFileHDF5 plugin saves the files to disk
Two files are generated:
  <name>-DET.h5 – detector data
  <name>-PANDABOX.h5 – position data
These are saved in a folder for each scan

## Slide 19: File Saving
NDFileHDF5 plugin saves the files to disk
Two files are generated:
  <name>-DET.h5 – detector data
  <name>-PANDABOX.h5 – position data
These are saved in a folder for each scan
Callbacks must be enabled

## Slide 20: File Saving
Images are buffered into a queue
If queue gets full -> frames are dropped!

## Slide 21: File Saving Configuration
HDF file structure defined in XML
  Configured by Malcolm
  Stored in the same directory as the scan data
  Deleted when the scan ends
Chunking parameters configured manually
  Defaults to the frame size if left at 0

## Slide 22: File Structure
The STATS plugin computes the total sum and attaches it as an NDAttribute
This is used to create the sum dataset
XML definition:
<dataset name="sum“ ndattribute="STATS_TOTAL“ source="ndattribute” />

## Slide 23: Frame Ordering
1 | 2 | 3
6 | 5 | 4
7 | 8 | 9
12 | 11 | 10
Remember: In a snake scan, alternate rows are captured backwards!

## Slide 24: Solution
Detector Driver
The NDPosPlugin intercepts the image frame and attaches the corresponding position as an attribute
The file saving plugin reads the position attributes and ensures the frames are stored in the correct order
NDPos Plugin
HDF5 Plugin
Raw data
Raw data + positions
XML Position data
1 | 2 | 3
6 | 5 | 4
7 | 8 | 9
12 | 11 | 10
Correctly ordered data
1
2
3
4
5
…
1 | (0,0)
2 | (0,1)
3 | (0,2)
4 | (1,2)
5 | (1,1)
… | 

## Slide 25: Unique Keys
When a dataset is extended, a ‘fill’ value is used
Q: How do we distinguish between fill and real data?
A: A special Unique Keys dataset is created:
  Same size as the scan dataset, with fill value 0
  A non-zero value is written when the corresponding scan data has been flushed to disk
  DAWN monitors this data set in order to know when to start processing a scan point

## Slide 26: h5watch
Command line tool for watching data added to a dataset
--dim option monitors for dimension size changes
h5watch --dim p45-164-DET.h5/entry/NDAttributes/NDArrayUniqueId
.h5 filename
HDF5 path to dataset
Opened "p45-164-DET.h5" with sec2 driver.
Monitoring dataset /entry/NDAttributes/NDArrayUniqueId...
dimension 0: 46->48 (increases)
dimension 1: 180->180 (unchanged)
dimension 2: 1->1 (unchanged)
dimension 3: 1->1 (unchanged)

## Slide 27: IOC Utilities
To reboot an IOC:
  console <IOC name> (remote IOCs)
  ioc-connect <IOC name> (test rig)
  Ctrl-X
To check what module versions are used:
  configure-ioc show <IOC name>
  Check the configure/RELEASE file

## Slide 28: IOC RELEASE File
# Common prefixes
SUPPORT = /dls_sw/prod/R3.14.12.3/support
WORK = /dls_sw/work/R3.14.12.3/support
# Module definitions
ADCORE = $(SUPPORT)/ADCore/2-6dls5
ADPANDABLOCKS = $(SUPPORT)/ADPandABlocks/2-0
ADSUPPORT = $(SUPPORT)/ADSupport/1-2
ARAVISGIGE = $(SUPPORT)/aravisGigE/2-1dls9
ASYN = $(SUPPORT)/asyn/4-31
BL46P_BUILDER = $(WORK)/BL46P-BUILDER
BUSY = $(SUPPORT)/busy/1-6-1dls1
CALC = $(SUPPORT)/calc/3-1
FFMPEGSERVER = $(SUPPORT)/ffmpegServer/3-1dls1-5
MOTOR = $(SUPPORT)/motor/6-9dls14
NORMATIVETYPESCPP = $(SUPPORT)/normativeTypesCPP/5-0-2
PMAC = $(SUPPORT)/pmac/2-1
PROCSERVCONTROL = $(SUPPORT)/procServControl/1-17-1
PVACCESSCPP = $(SUPPORT)/pvAccessCPP/4-1-3
PVDATABASECPP = $(SUPPORT)/pvDatabaseCPP/4-1-1
PVDATACPP = $(SUPPORT)/pvDataCPP/5-0-4
# EPICS Base appears last
EPICS_BASE = /dls_sw/epics/R3.14.12.3/base
AreaDetector modules