## Slide 1: Hardware Triggered Scanning: Malcolm
Philip Taylor, Emma Arandjelovic
Observatory Sciences Limited

## Slide 2: Software Stack: Reminder
Data Analysis WorkbeNch
- Analysis and visualization
Generic Data Acquisition
- Experiment setup and supervision
Malcolm
- Scan configuration
Experimental Physics & Industrial Control System
- Low level control of hardware

## Slide 3: What is Malcolm?
Generic and extensible framework for scanning
Middle layer between GDA and control system
Implemented in
Creates a s/w map of the h/w layer
https://pymalcolm.readthedocs.io
Web GUI called MalcolmJS
https://malcolmjs.readthedocs.io

## Slide 4: Malcolm Process
Each Malcolm instance is a Python process managed by procServ
On beamlines this runs on ixx-control
[p47user@localhost ]$ ioc-list
BL47P-EA-IOC-01: pid = 2628, telnet port = 7002
BL47P-ML-MALC-01: pid = 2663, telnet port = 7003
To reboot:
ioc-connect BL4xP-ML-MALC-01
Ctrl-X

## Slide 5: Malcolm Concepts
Process
Block
method1()
attribute1
Block
method1()
attribute1
A block is a user-centred view
  Examples:
  Motion controller
  PandA
  Detector
  ‘Hello World’ program
Blocks contain:
  Methods (actions)
  Attributes (data)
A process hosts multiple blocks
Parent blocks contain child blocks connected together in a design

## Slide 6: Malcolm Concepts
Each block has a unqiue name called an MRI (Malcolm Resource Identifier) e.g. BL47P-ML-SCAN-01
A device block is a higher level block for synchronizing a number of child blocks
Motion Controller Block
X stage block
Y stage block
Co-ordinate system block

## Slide 7: Malcolm Concepts
A runnable device block adds state machine functionality with two main methods:
configure(params)
  – setup all child blocks
run()
  – start all children and supervise their progress
Simplified runnable device block state machine

## Slide 8: Control Flow
Two step process:
Configure the scan
Run the scan

## Slide 9: Web GUI: Overview
Central panel: design layout / attribute view
Right: inspector
Left: parent block (in focus)

## Slide 10: Web GUI: Block View
Attributes displayed depend on the type of block
Tool-tip text provide descriptions
Any problems connecting to the h/w are displayed in the tool-tip

## Slide 11: Web GUI: Attribute View
Displays table or plot of historical data values

## Slide 12: Web GUI: Layout View
Graphical view of selected root block, with automatic layout feature

## Slide 13: Web GUI: Layout View
‘Wire-up’ components visually

## Slide 14: Web GUI: Layout View
Palette – drag and drop new items
Auto Layout – first step for complex layouts

## Slide 15: Web GUI: Navigation
Starting with the selected root block, you can drill down into the design
Breadcrumb trail in central panel

## Slide 16: Web GUI: Navigation
Example: select BRICK in the layout view
Then choose Layout in the right hand inspector

## Slide 17: Web GUI: Navigation
Now focused on the BRICK block:
  Controller
  Trajectory
  Co-ordinate system
  Axes
  Status

## Slide 18: Web GUI: Navigation
Now focused on the BRICK block:
  Controller
  Trajectory
  Co-ordinate system
  Axes
  Status
Select STATUS

## Slide 19: Web GUI: Navigation

## Slide 20: Exercise: Web GUI
Navigate to the PANDA block
Try to toggle on/off the light controlled by TTLOUT2
For more info on the web GUI: https://malcolmjs.readthedocs.io

## Slide 21: Designs
Different scan requirements can be implemented using multiple designs
Example: a new experiment requires a different PandA configuration
Step 1: Open the PANDA block in the layout view
Step 2: Modify the design as required
Step 3: Choose a name and save

## Slide 22: Designs
Step 4: Open the SCAN block layout
Step 5: Select the PANDABOX and choose the new design

## Slide 23: Designs
Step 6: Using the left hand panel, save this SCAN configuration as a new design

## Slide 24: Designs
To load a design in the Web GUI:
Navigate to the root block
Select the design from the drop down list in the left hand panel

## Slide 25: Malcolm Configuration
Blocks are reusable components that require configuration
  Examples:
  PV prefix (for EPICS devices), IP address (for PandA)
  Initial design
  Runtime config directories
Configuration specified in YAML
  (‘YAML Ain’t Markup Language’!)

## Slide 26: YAML Files

## Slide 27: YAML Files

## Slide 28: YAML Files

## Slide 29: Exercise: pvAccess
Malcolm<->GDA interface uses pvAccess (EPICS V4)
Each block is represented as a V4 process variable (pv) with a number of fields
Use pvget to dump the entire SCAN block structure
  pvget BL4xP-ML-SCAN-01 -r “”
(If pvget not in PATH, run module load pvatools)

## Slide 30: pvAccess continued
-r ‘request’ option specifies which fields to return
      pvget BL4xP-ML-SCAN-01 –r health.value
What information comes back for the layout field?
Other useful SCAN block fields include:
  totalSteps
  completedSteps
  state

## Slide 31: Exercise: Scan States
Start a scan in GDA and monitor the SCAN block in the Malcolm web GUI. What states does it go through?
The -m (‘monitor’) option to pvget monitors the PV for changes. Use this together with the –r option to monitor the completedSteps field from the command line as the scan progresses.

## Slide 32: Scan States Screenshot

## Slide 33: Dataset table