## Slide 1: Hardware Triggered Scanning: GDA and DAWN
Philip Taylor, Emma Arandjelovic
Observatory Sciences Limited

## Slide 2: Software Stack: Reminder
Data Analysis WorkbeNch
- Analysis and visualization
Generic Data Acquisition
- Experiment setup and supervision
Malcolm
- Scan configuration
Experimental Physics & Industrial Control System
- Low level control of hardware

## Slide 3: Overview
Main beamline user interface
Presents a science based view of experiments
Client-server design
Command Server provides a Jython interpreter
Client provides live data visualization
EPICS control system
GDA server
ixx-control
Command Server
Channel Access
GDA client
workstation
Data Vis.
GDA client
workstation
Data Vis.
Java RMI

## Slide 4: Overview
Main beamline user interface
Presents a science based view of experiments
Client-server design
Command Server provides a Jython interpreter
Client provides live data visualization
GDA<->Malcolm interface developed to integrate scanning framework
EPICS control system
GDA server
ixx-control
Command Server
Java RMI
Channel Access
Malcolm
pvAccess
Channel Access
GDA client
workstation
Data Vis.
GDA client
workstation
Data Vis.

## Slide 5: Overview
Data Analysis WorkbeNch
Sister project to GDA (Eclipse based)
Provides visualization components to GDA client
Includes generic data processing tools
Data processing pipelines can be customized
Supports multiple file formats, including NeXus
See https://dawnsci.org/

## Slide 6: Data Flow
GDA Server
GDA Client
DAWN Processing
EPICS AreaDetector
DAWN visualization
Raw HDF5 data
NeXus metadata
Processed NeXus files
DAWN webserver
POSIX compliant file system
Data written to a POSIX file system
  Enables SWMR mode

## Slide 7: Data Flow
GDA Server
GDA Client
DAWN Processing
EPICS AreaDetector
DAWN visualization
Raw HDF5 data
NeXus metadata
Processed NeXus files
DAWN webserver
POSIX compliant file system
Data written to a POSIX file system
  Enables SWMR mode
AreaDetector writes raw HDF data

## Slide 8: Data Flow
GDA Server
GDA Client
DAWN Processing
EPICS AreaDetector
DAWN visualization
Raw HDF5 data
NeXus metadata
Processed NeXus files
DAWN webserver
POSIX compliant file system
Data written to a POSIX file system
  Enables SWMR mode
AreaDetector writes raw HDF data
GDA writes metadata to another HDF file

## Slide 9: Data Flow
GDA Server
GDA Client
DAWN Processing
EPICS AreaDetector
DAWN visualization
Raw HDF5 data
NeXus metadata
Processed NeXus files
DAWN webserver
POSIX compliant file system
Data written to a POSIX file system
  Enables SWMR mode
AreaDetector writes raw HDF data
GDA writes metadata to another HDF file
The two HDF files are linked

## Slide 10: Data Flow
GDA Server
GDA Client
DAWN Processing
EPICS AreaDetector
DAWN visualization
Raw HDF5 data
NeXus metadata
Processed NeXus files
DAWN webserver
POSIX compliant file system
Data written to a POSIX file system
  Enables SWMR mode
AreaDetector writes raw HDF data
GDA writes metadata to another HDF file
The two HDF files are linked
DAWN processing reads both files

## Slide 11: Data Flow
GDA Server
GDA Client
DAWN Processing
EPICS AreaDetector
DAWN visualization
Raw HDF5 data
NeXus
metadata
Processed NeXus files
DAWN webserver
POSIX compliant file system
Data written to a POSIX file system
  Enables SWMR mode
AreaDetector writes raw HDF data
GDA writes metadata to another HDF file
The two HDF files are linked
DAWN processing reads both file
DAWN webserver makes the raw and processed files available to the GDA client outside the POSIX file system

## Slide 12: Interface to Malcolm
Malcolm<->GDA interface uses pvAccess (EPICS V4)
This supports structured data
Each Malcolm ‘device’ in GDA maps onto a block:
  $(gda_config)/servers/main/live/malcolm_real.xml
This defines the MRI (Malcolm Resource Identifier) for the top level scan block

## Slide 13: Interface Customization
$(gda_config)/clients/main/_common/mapping.xml
Axis name labels:
Outer scan axes:

## Slide 14: GDA perspectives
GDA has three main perspectives you’ll use with Malcolm:
Mapping
DataVis
  Used both of these in Part 1
Processing
A perspective is a collection of related views

## Slide 15: Mapping Perspective
Mapping perspective used for:
Setting up scan ‘map’
Configuring sample metadata
Start/stop/pause controls
Monitoring progress
Viewing results

## Slide 16: Mapping Experiment Setup
Configure any outer scan axes

## Slide 17: Mapping Experiment Setup
Configure any outer scan axes
Select the Malcolm device and enter desired exposure time

## Slide 18: Mapping Experiment Setup
Configure any outer scan axes
Select the Malcolm device and enter desired exposure time
Choose desired region shape and scan path

## Slide 19: Mapping Experiment Setup
Configure any outer scan axes
Select the Malcolm device and enter desired exposure time
Choose desired region shape and scan path
Configure the map region
  Manually

## Slide 20: Mapping Experiment Setup
Configure any outer scan axes
Select the Malcolm device and enter desired exposure time
Choose desired region shape and scan path
Configure the map region
  Manually, or
  By drawing desired shape

## Slide 21: Mapping Experiment Setup
Map points calculated automatically
Save/load/copy command to clipboard
Add scan to queue
Choose a processing template

## Slide 22: Mapping Queue
Scan ‘jobs’ are put into a queue and started automatically
Error messages displayed here
Re-order / pause / abort jobs
View status and progress

## Slide 23: Mapped Data View
Lists the generated NeXus (.nxs) files
The sum dataset is created by summing the pixel values over the whole image
If processing was selected, a processed file is also generated

## Slide 24: Map View
Displays single pixel per scan point
As the sample is rotated, the camera captures a different angle
This results in an approximate sinewave for each sample ‘stick’
Example: representation of the sum (total intensity) data set

## Slide 25: Map View
Scans can be performed over the top of each other
Use case: scan a small area in higher resolution

## Slide 26: Detector Data View
Click a point in the map view
Detector data view updates to show corresponding detector frame

## Slide 27: Live Mapping
The mapping perspective updates raw and processed data as the scan progresses
This is done via a DataServer on ixx-control (localhost on the test rig)
Can check this using http requests in a browser:
  http://localhost:8690/tree/?path=<path2nxsfile>
    Displays the NeXus tree as XML
  http://localhost:8690/info/?path=<path2nxsfile>&dataset=<dataset>
    Displays information about the specified dataset e.g. /entry/DET/data
  http://localhost:8690/slice/?path=<path2nxsfile>&dataset=<dataset>&slice=[0,0,:,:]
    Downloads data in specified slice as zip file
When scan finished, file loaded directly from disk

## Slide 28
https://dawnsci.org/assets/pages/using_dawn/MappingCheatSheet.pdf

## Slide 29: DataVis Perspective
Use the File menu to load data files and select for viewing
Datasets view shows the available datasets in the selected file and their dimensions
Standalone perspective provided by DAWN
Can be used to open any HDF file
Can also be used at runtime to display additional datasets e.g. UniqueKeys

## Slide 30: DataVis Perspective
Check the box on both the file AND dataset to activate it for display

## Slide 31: DataVis Perspective
Choose how to display the selected dataset from the dropdown
Assign axes to each dimension

## Slide 32
https://dawnsci.org/assets/pages/using_dawn/DataVisCheatSheet.pdf

## Slide 33: Live Processing
Add new processing
Live setup
Load existing pipeline

## Slide 34: Live Processing

## Slide 35: Live Processing
Set range

## Slide 36
https://dawnsci.org/assets/pages/using_dawn/ProcessingCheatSheet.pdf

## Slide 37: Exercise: Make your own mean integration pipeline
Open the mean_integrate.nxs file you used for the live processing in Part 1 and inspect it
Clear the pipeline, and then recreate it using the star button to add processing steps
Save it with a distinct name somewhere obvious
Start a new scan using the old mean_integrate.nxs template, and the one you just created
Hopefully they produce the same result!
Play around with other processing steps (e.g. Gaussian filter)

## Slide 38: Live Processing
GDA can submit pipelines to DAWN for live processing
Publish-subscribe mechanism using ActiveMQ
Other subscribers can also be written e.g. using Python
Scan Status Topic
Scan started
GDA server
DAWN consumer
Scan started
Sends message
Delivers message
Subscribes

## Slide 39
ActiveMQ Web console on port 8161
Processing topic
Scan topic
‘Processing finished’ message triggers final reconstruction

## Slide 40: Live Processing - Details
DAWN consumer receives a JSON message on scan start and writes it to disk:
  {visit folder}/tmp/operationBean.json
JSON file contains the path to the scan data files
Consumer then starts a new DAWN process on the cluster which reads the JSON file
Log files also stored in {visit folder}/tmp
Note: Test rig is setup slightly differently

## Slide 41: Live Processing - Details
On beamlines, the DAWN Consumer and ActiveMQ processes run on ixx-control
On the test rig, ActiveMQ runs under ProcServ:
  ioc-connect BL4xP-EA-PRCO-01
  Ctrl-X to reboot

## Slide 42: More flexible processing
Status information about the scan is sent to an ActiveMQ topic: gda.messages.scan
A script can subscribe to this topic to do arbitrary processing during or after a scan
See visualhulls for an example
There is a python3 module called scansubscriber to help

## Slide 43: Watchdogs
Watchdogs provide a mechanism to pause and resume a scan based on an external condition
General case: ExpressionWatchdog
  ring_current >= 1.0 && !portshutter.equals(‘Closed’)
  scannable names comparision and literals
  logical operators
  Scan paused when expression becomes FALSE
Special case: TopupWatchdog
  Monitors SR-CS-FILL-01:COUNTDOWN
  Configurable warmup and cooloff periods (ms)

## Slide 44: Configuring Watchdogs
ExpressionWatchdog:
<bean id=“noBeam" class="org.eclipse.scanning.api.device.models.DeviceWatchdogModel">
<property name="expression" value="ring_current >= 1.0"
<property name="message" value="Beam has been lost"/>
</bean>
TopupWatchdog:
<bean id=“beamTopup" class="org.eclipse.scanning.api.device.models.DeviceWatchdogModel">
<property name="countdownName" value="machineTopupMonitor"/>
<property name="message" value="Paused during topup"/>
<property name="warmup" value="5000"/>
<property name="cooloff" value="4000"/>
<property name="modeName" value="ringModeMonitor"/>
</bean>
Create an instance of DeviceWatchdogModel
  Give it an ID (name)
  Define the properties (dependent on the type of watchdog)
  Ensure it’s linked to by the GDA server configuration

## Slide 45: Configuring Watchdogs
Example: ExpressionWatchdog
<bean id=“noBeam" class="org.eclipse.scanning.api.device.models.DeviceWatchdogModel">
<property name="expression" value="ring_current >= 1.0"
<property name="message" value="Beam has been lost"/>
</bean>
<bean id="expressionWatchdog" class="org.eclipse.scanning.sequencer.watchdog.ExpressionWatchdog“ init-method="activate">
<property name="model" ref=“noBeam"/>
<property name="enabled" value="true" />
</bean>
Create an ExpressionWatchdog or TopupWatchdog instance and link it to the model

## Slide 46: Watchdogs
Watchdogs are controlled at run time via the Jython console:
enableWatchdogs()
disableWatchdogs()
listWatchdogs()

## Slide 47: Logs
  On the test rig, GDA logs are stored here:
    /dls_sw/p4x/software/gda_logs
  But can use the GDA log monitor from launcher or:
  > module load gdalogpanel
  > gdalogpanel
  EPICS logs are in the IOC:
    /dls/p4x/epics/logs/BL4xP-EA-IOC-01
DAWN processing logs can be found here:
  /dls/p4x/epics/logs/BL4xP-EA-PRC0-0x

## Slide 48: Practical Exercises
The scripts located in /localhome/p4xuser/training each trigger a problem somewhere in the stack…
Restart the machine to ensure a fresh start and confirm scans are working
Run one of the scripts
Start a new scan from GDA
Try to figure out what goes wrong and how to fix it!
No cheating!