## Slide 1: Hardware Triggered Scanning: Scanning Components
Philip Taylor, Emma Arandjelovic
Observatory Sciences Limited

## Slide 2: Overview
To perform scans, we need to control complex devices such as motion controllers and detectors
This topic will cover how these devices are configured by Malcolm
We will use a simulated motion controller and detector to see how this works in practice
We will also look at how to generate scan trajectories

## Slide 3: Block Structure
Blocks like we have created so far make up the lowest level of blocks, known as the Hardware Layer
The Device Layer is a higher level of blocks that synchronise a number of child blocks to create an interface to a device e.g. a detector or motor controller
Motion Controller Block
X stage block
Y stage block
Co-ordinate system block
Device Layer
Hardware Layer
Example:

## Slide 4: Device Blocks
Device blocks instantiate one or more child blocks
A controller aimed at managing child blocks is called a ManagerController
This provides:
  A layout of child blocks
  A mechanism to enable / disable child blocks
  A mechanism to load / save designs (saved configurations)
State machine:

## Slide 5: Motion Demo
Two Counter blocks in the hardware layer simulate motor axes (X and Y)
A device block called Motion simulates a motor controller with XMove and YMove methods
The Counter blocks are constructed with BasicControllers
The Motion block is constructed with a ManagerController
See the Motion tutorial: https://pymalcolm.readthedocs.io/en/latest/tutorials/motion.html

## Slide 6: Motion Block Definition
- builtin.controllers.ManagerController:
mri: $(mri)
config_dir: $(config_dir)
description: $(docstring)
- demo.blocks.counter_block:
mri: $(mri):COUNTERX
- demo.blocks.counter_block:
mri: $(mri):COUNTERY
- demo.parts.CounterMovePart:
name: x
mri: $(mri):COUNTERX
- demo.parts.CounterMovePart:
name: y
mri: $(mri): COUNTERY
demo/blocks/motion_block.yaml (extract):
Use a ManagerController to construct the block
  This takes an additional parameter to specify a directory for saving configurations
Instantiate two Counter blocks
Instantiate two MotorMove parts, one per block

## Slide 7: Motion Example Structure
Notice the design attribute and save method are contributed by the ManagerController

## Slide 8: Designs
Recall: Designs allow you to save the layout of a device block and the attributes of its child blocks

## Slide 9: Designs continued
Which attributes are saved?
Recall the attribute definition in our Counter part:
self.counter = NumberMeta(
"float64", "The current value of the counter",
tags=[config_tag(), Widget.TEXTINPUT.tag()])
Tags contain important metadata:
  Widget tags - choose which widget to display it with
  Group tags - create an expander around related attributes
  Port tags - create the visual connections between blocks
  Config tags - turn on saving/loading
See: https://pymalcolm.readthedocs.io/en/latest/reference/tags.html

## Slide 10: How to Create a Device Part
Subclass builtin.parts.ChildPart
  This provides access to the child blocks
Create annotypes for any variables we need
Create an __init__() method:
  Call super().__init__()
Create a setup() method:
  Call super().setup()
  Register any additional methods and attributes
Implement the methods to perform the business logic
  Use the passed in context to access the child block

## Slide 11: Motor Move Part Definition
demo/parts/countermovepart.py (extract):
with Anno("The demand value to move our
counter motor to"):
ADemand = float
@builtin.util.no_save(“counter”)
class CounterMovePart(builtin.parts.ChildPart):
def __init__(self, name, mri):
# type: (APartName, builtin.parts.AMri) -> None
super(CounterMovePart, self).__init__(name, mri, initial_visibility=True, stateful=False)
def setup(self, registrar):
# type: (PartRegistrar) -> None
super(CounterMovePart, self).setup(registrar)
registrar.add_method_model(self.move,
self.name + “Move”, needs_context=True)
Create an Annotype for the demand position
Define attributes in the child block not to be saved
Call super().__init__()
Register the method model in setup, ensuring the name is unique for each part
Tell Malcolm the method needs a Context object for accessing the child block

## Slide 12: Part Definition Continued
demo/parts/countermovepart.py (continued):
@add_call_types
def move(self, context, demand):
# type: (builtin.hooks.AContext, ADemand) -> None
child = context.block_view(self.mri)
child.counter.put_value(demand)
Use the passed in context as well as the MRI to create a Block view of the Counter child Block
Set the Block’s counter attribute to the new demand

## Slide 13: Running the Motion Demo
./malcolm/imalcolm.py malcolm/modules/demo/DEMO-MOTION.yaml
Open http://localhost:8008/
Select the MOTION:COUNTERX block and ‘tear-off’
Repeat for MOTION:COUNTERY
Select the MOTION root block and request new values for X and Y
Watch the counter blocks changing value
Practise saving and loading designs with different delta values

## Slide 14: Detector Demo
A dummy detector that takes a scan specification and writes data to an HDF5 file
This will introduce two new concepts:
  RunnableController – provides methods and attributes relating to the different steps of a scan
  ScanPointGenerator – used to generate n-dimensional scan paths
See the Detector tutorial: https://pymalcolm.readthedocs.io/en/latest/tutorials/detector.html

## Slide 15: Runnable Device Blocks
A ‘Runnable’ device block understands what a scan is
It has a state machine that implements the scan process
This is controlled by the user via two important methods:
  configure()
    Configure all child blocks according to the supplied parameters
  run()
    Start all child blocks running, provide status monitoring and periodic actions
These are contributed to the block by a RunnableController

## Slide 16: Runnable Controller Details
Inherits from ManagerController
Adds to the ManagerController state machine to include the different steps of a scan
Additional attributes:
  completedSteps
  configuredSteps
  totalSteps
Controllers provide hooks, which Parts can register with to run the device specific logic on state transitions

## Slide 17: Runnable Controller States
Hooks are run on state transitions
See: https://pymalcolm.readthedocs.io/en/latest/reference/statesets.html#statesets

## Slide 18: Hooks Overview
Functions registered to hooks are called automatically by the controller
All functions hooked to the same hook are called concurrently
Examples:
  ConfigureHook (part, context, completed_steps, steps_to_do, part_info, generator, axesToMove, **kwargs):
    Called at configure() to setup a child block
  RunHook (part, context, **kwargs):
    Called at run() to start all children running
  ResetHook(part)
    Called at reset() to return to Ready state

## Slide 19: Runnable Device Sequence Diagrams
Note: There are more hooks than are shown here, see https://pymalcolm.readthedocs.io/en/latest/reference/statesets.html for a complete list of hooks.

## Slide 20: Detector Demo Structure
The DETECTOR block is constructed with a RunnableController
A FileWritePart writes the HDF5 file
  Configure hook takes a scan point generator and initialises the scan
  Run hook iterates through the generator points and writes the data
A DatasetTablePart collects info (location, size etc.) about the data and exposes it in the datasets attribute

## Slide 21: Detector Block Definition
- builtin.controllers.RunnableController:
mri: $(mri)
config_dir: $(config_dir)
description: $(docstring)
- builtin.parts.LabelPart:
value: $(label)
- scanning.parts.DatasetTablePart:
name: DSET
- demo.parts.FileWritePart:
name: FW
width: 160
height: 120
demo/blocks/detector_block.yaml (extract):
Use a RunnableController to construct the block
A LabelPart displays a title on the GUI
A DatasetTablePart reports the datasets written
  A FileWritePart writes some dummy data to an HDF5 file

## Slide 22: Detector Demo Sequence Diagram
This demo detector saves some generated data to an HDF5 file just as an example.

## Slide 23: How to Create a Runnable Device Part
Subclass builtin.parts.Part or builtin.parts.ChildPart
Create an __init__ method:
  Call super().__init__()
Implement the on_configure(*params), on_run() and reset() methods to perform the business logic
  The on_configure method should prepare the scan
  The on_run method should generate the data and report progress to the controller so it can update the block’s currentStep attribute
  The reset method should clean up after a scan, even if it failed.
Create a setup method:
  Register any additional methods and attributes
  Register any hooks with the controller
  Inform the controller what extra parameters configure requires

## Slide 24: File Write Part: init
demo/parts/filewritepart.py (extract):
class FileWritePart(Part):
def __init__(self, name, width, height):
# type: (APartName, AWidth, AHeight) -> None
super(FileWritePart, self).__init__(name)
# Store input arguments
self._width = width
self._height = height
# The detector image we will modify for each image (0..255 range)
self._blob = make_gaussian_blob(width, height) * 255
# The HDF5 file we will write
self._hdf = None # type: h5py.File
# Configure args and progress info
self._generator = None # type: scanning.hooks.AGenerator
self._completed_steps = 0
self._steps_to_do = 0
# How much to offset unique id value from generator point (for rewind function)
self._uid_offset = 0

## Slide 25: Detector Demo Sequence Diagram
This demo detector saves some generated data to an HDF5 file just as an example.

## Slide 26: File Write Part: on_configure
demo/parts/filewritepart.py (extract):
def on_configure(self,
completed_steps, # type: scanning.hooks.ACompletedSteps
steps_to_do, # type: scanning.hooks.AStepsToDo
generator, # type: scanning.hooks.AGenerator
fileDir, # type: scanning.hooks.AFileDir
formatName="det", # type: scanning.hooks.AFormatName
fileTemplate="%s.h5", # type: scanning.hooks.AFileTemplate
):
# type: (...) -> scanning.hooks.UInfos
# Store the parameters and create an empty HDF file
self._generator = generator
filename = fileTemplate % formatName
filepath = os.path.join(fileDir, filename)
self._hdf = self._create_hdf(filepath, generator)
# Create the Info objects describing the two datasets…..
infos = [scanning.infos.DatasetProducedInfo(name=…) ,…]
return infos

## Slide 27: Detector Demo Sequence Diagram
This demo detector saves some generated data to an HDF5 file just as an example.

## Slide 28: File Write Part: on_run
def on_run(self, context):
# type: (scanning.hooks.AContext) -> None
"""On `RunHook` record where to next take data"""
end_of_exposure = time.time() + self._exposure # Start time so everything is relative
last_flush = end_of_exposure
for i in range(self._completed_steps, self._completed_steps + self._steps_to_do):
point = self._generator.get_point(i)
wait_time = end_of_exposure - time.time()
context.sleep(wait_time) # Must use the context parameter to make it
# an interruptible sleep so the scan can be aborted
self.log.debug("Writing data for point %s", i)
self._write_data(point, i)
if time.time() - last_flush > FLUSH_PERIOD:
last_flush = time.time()
self._flush_datasets()
end_of_exposure += point.duration
self.registrar.report(scanning.infos.RunProgressInfo(i + 1))
self._flush_datasets()
demo/parts/filewritepart.py (extract):

## Slide 29: Detector Demo Sequence Diagram
This demo detector saves some generated data to an HDF5 file just as an example.

## Slide 30: File Write Part: reset
demo/parts/filewritepart.py (extract):
def on_reset(self):
# type: () -> None
if self._hdf:
self._hdf.close()
self._hdf = None

## Slide 31: File Write Part: setup
demo/parts/filewritepart.py (continued):
def setup(self, registrar):
# type: (PartRegistrar) -> None
super(FileWritePart, self).setup(registrar)
# Hooks
registrar.hook(scanning.hooks.ConfigureHook, self.on_configure)
registrar.hook((scanning.hooks.PostRunArmedHook,
scanning.hooks.SeekHook), self.on_seek)
registrar.hook(scanning.hooks.RunHook, self.on_run)
registrar.hook((scanning.hooks.AbortHook,
builtin.hooks.ResetHook), self.on_reset)
# Tell the controller to expose some extra configure parameters
registrar.report(scanning.hooks.ConfigureHook.create_info(self.on_configure))

## Slide 32: Additional Hooks
More examples:
SeekHook
  Used for pause/rewind functionality, to adjust the completed_steps
PostRunArmedHook
  Called at the end of run() when there are more steps to be run
    (e.g. when the scan is paused)
AbortHook
  Called at abort() to stop the current scan
ResetHook
  Called at reset() to reset all Parts to a known state

## Slide 33: Info Objects
An Info is an object created by a Part and passed to its parent Controller in one of two ways:
  Returned from a hooked function
  Reported via PartRegistrar.report(info)
  We report progress via PartRegistrar.report(info) in the method registered to the RunHook:
def on_run(self, context): … for i in range(…): … self.registrar.report( scanning.infos.RunProgressInfo(i+1))

## Slide 34: Info Objects Continued
We return a description of the dataset produced by the Part from the method registered to the ConfigureHook:
def on_configure(self, …): # type: (...) -> scanning.hooks.UInfos … infos = [scanning.infos.DatasetProducedInfo(name=…), …] return infos
DatasetProducedInfo parameters:
  name – Dataset name
  filename – Filename relative to the fileDir we were given
  type – What NeXuS dataset type it produces
  rank – The rank of the dataset including generator dims
  path – The path of the dataset within the file
  uniqueid – The path of the UniqueID dataset within the file

## Slide 35: Info Objects Continued
    We report additional arguments for hook functions in the setup method:
      def setup(self, registrar):
      …
      registrar.report(
      scanning.hooks.ConfigureHook.create_info(self.configure))
create_info scans the on_configure method for the arguments in addition to completed_steps and steps_to_do:
  generator
  fileDir
  formatName
  fileTemplate

## Slide 36: Detector Demo
A dummy detector that takes a scan specification and writes data to an HDF5 file
This will introduce two new concepts:
  RunnableController – provides methods and attributes relating to the different steps of a scan
  ScanPointGenerator – used to generate n-dimensional scan paths
See the Detector tutorial: https://pymalcolm.readthedocs.io/en/latest/tutorials/detector.html

## Slide 37: Scan Point Generator
To run a continuous scan, we need many parameters:
  Demand positions for frame midpoint
  Demand positions for frame start and end
  Index at which to store the frame
  Duration of the frame
A Python module called ScanPointGenerator generates this data for a variety of scan types (e.g. line, spiral, …)
A generator is passed to the configure method to setup the scan
See https://scanpointgenerator.readthedocs.io

## Slide 38: Scan Point Generator Example
class scanpointgenerator.LineGenerator
(axes, units, start, stop, size, alternate=False)
- Generate a line of equally spaced N-dimensional points
Parameters:
axes (str/list(str)) – The scannable axes E.g. “x”
units (str/list(str)) – The scannable units. E.g. “mm”
start (float/list(float)) – The first position to be generated. e.g. 1.0
stop (float/list(float)) – The final position to be generated. e.g. 5.0
size (int) – The number of points to generate. E.g. 5
alternate (bool) – Specifier to reverse direction

## Slide 39: Preparing the Example
./malcolm/imalcolm.py malcolm/modules/demo/DEMO-DETECTOR.yaml
>>> from scanpointgenerator import LineGenerator, CompoundGenerator
>>> from scanpointgenerator.plotgenerator import plot_generator
>>> yline = LineGenerator("y", "mm", -1, 0, 6)
>>> xline = LineGenerator("x", "mm", 4, 5, 5, alternate=True)
>>> generator = CompoundGenerator([yline, xline], duration=0.5)
>>> plot_generator(generator)
>>> from annotypes import json_encode
>>> json_encode(generator)
Copy the JSON output to the clipboard

## Slide 40: Running the Example
Open http://localhost:8008/gui/DETECTOR
Expand the Configure method and Edit the generator field to paste in the JSON code
Set the fileDir to /tmp
Click Configure
Click Run
Watch the Completed Steps counter increase

## Slide 41: Checking the Results
>>> import h5py
>>> with h5py.File(“/tmp/det.h5”) as f:
….: im = f[“/entry/sum”][:]
….:
>>> im.shape
(6, 5, 1, 1)
>>> from pylab import imshow, show
>>> imshow(im[:, :, 0, 0])
<matplotlib.image.AxesImage at 0x7f11b090>
>>> show()

## Slide 42: Recap: yaml chains

## Slide 43: Recap: yaml chains

## Slide 44: Practical Exercises
Modify the Motion demo to add high and low soft limits (values to be provided in DEMO-MOTION.yaml). If a demand is requested out of this range, it should raise an error. Provide default values of 0, meaning soft limits are disabled. Hint 1: Start by modifying the DEMO-MOTION.yaml file and work your way down. Hint 2: Read the docs! See builtin parameter types from second page: https://pymalcolm.readthedocs.io/en/latest/tutorials/motion.html https://pymalcolm.readthedocs.io/en/latest/build/builtin/parameters_api.html
Modify the generator in the Detector demo to create a larger and faster scan.